| Mazda Familia 1993 |  |
| --- | --- |

### Modification GT, produced from 1993 (february)

| GENERAL |
| --- |
| Body type | Sedan |
| Drive | FF |
| Transmission | 5 speed manual |
| Displacement, cc | 1839 |
| Frame | E-BG8P-FHC |
| Price of new car, thousands yen (Tokyo area) | 1783 (~$14800) |
| SPECIFICATION (SPECS) |
| EXTERIOR |
| Exterior dimensions (LxWxH), mm | 4250 x 1690 x 1375 |
| Interior dimensions (LxWxH), mm | 1775 x 1385 x 1145 |
| Wheel base, mm | 2500 |
| Treads (F/R), mm | 1430 / 1435 |
| Ground clearance, mm | 150 |
| Curb vehicle weight, kg | 1070 |
| Seating capacity, persons | 5 |
| Doors number | 4 |
| Min.turning radius, m | 4.8 |
| Fuel tank capacity, l | 50 |
| ENGINE |
| Displacement, cc | 1839 |
| Engine model | BP |
| Max.power (Net), kw(PS)/rpm | 135 ps (99.29 kw) / 7000 rpm |
| Max.torque(Net), N*m(kg*m)/rpm | 16.0 kg*m (156.91 N*m) / 4500 rpm |
| Power density | 7.93 |
| Engine type | Water cooling serial 4 cylinder DOHC16 valve |
| Fuel system | EGI |
| Turbocharger | No |
| Fuel type | Unleaded regular gasoline |
| LEV system (Low emission vehicle) | No |
| Compression ratio | 9 |
| Bore, mm | 83 |
| Stroke, mm | 85 |
| Final gear ratio |  |
| Fuel consumption at 10-15 modes, l/100km | 8.6 |
| CHASSIS / TRANSMISSION |
| Power steering | Yes |
| Tires size, front | 185/60R14 82h |
| Tires size rear | 185/60R14 82h |
| Braking system, front | Ventilated disk |
| Braking system, rear | Disk |
| Suspension system, front | Strut type independent suspension |
| Suspension system, rear | Strut type independent suspension |
| EQUIPMENT |
| EXTERIOR EQUIPMENT |
| Sunroof / Moonroof |  |
| Front fog lamp |  |
| Rear fog lamp |  |
| Xenon headlight (Discharge lamp) |  |
| Projector headlight |  |
| Rear wiper |  |
| Front spoiler |  |
| Rear or roof spoiler |  |
| ABS (Antilock brake system) |  |
| LSD (Limited slip differential) |  |
| Privacy glass |  |
| UV cutting glass |  |
| Aluminium wheel | 14 inch standard |
| INTERIOR EQUIPMENT |
| Air conditioner | Full automatic |
| Wood panel |  |
| Cruise control |  |
| Centralized door lock |  |
| Power window |  |
| Steering wheel telescopic |  |
| Steering wheel tilt |  |
| Leather steering wheel |  |
| Leather seat |  |
| Falling down type rear seat | Divided type |
| Child seat fixed with seat belt |  |
| Rear ELR3 point seat belt |  |
| Front seat pretensioner seat belt |  |
| Fourth limited front seat belt |  |
| Side impact bar |  |
| Airbag (Driver) |  |
| Airbag (Passenger) |  |
| Airbag (Side) |  |
| Audio deck | AM/FM radio equipped cassette player |

- present - not present - option